## Slide 1: SDB Predicting Energy Usage at 88acres
Mike Wise
Version 0.7
19 Aug 2015

## Slide 2: SDB Business Goals
Energy Usage Prediction
  Planning and Hedging Energy Purchasing Strategies
  Predicting and Mitigating Peak Energy usage to reduce Demand Charges
Predictive Maintenance
  Recalibrating fault importance
  Measuring impact of equipment performance on Energy and Indoor Climate
  Predicting equipment outages

## Slide 3: Typical Building Usage Profile

## Slide 4: Typical Electric Bill with Usage/Demand Charges
Usage
Demand

## Slide 5: Yearly Financial Impact

## Slide 6: Project Resources
1 TB of data – HVAC, Energy Usage, and some temperature data
Azure Account
  SQL VM
  Hadoop cluster
  AML Workspace
1 full-time MCS Architect/DS Resource (Mike)
1 part-time (1.5 d/w) AML PG DS Resource (Girish)

## Slide 7: Compute Landscape

## Slide 8: SDB – The Data Science
CRISP-DM – best developed DS methodology
  Little competition
6 Phases
  Business Understanding
  Data Understanding
  Data Preparation
  Data Modelling
  Evaluation
  Deployment

## Slide 9: Time Line
4-5 months on project so far
Main project directory has 6000+ files in 62 folders

## Slide 10: SDB Business Understanding - Overview
Actual Business Benefits articulated
Revisited at least twice during project
Initial focus was Pred.Maint. oriented, shifted to an Energy Focus
  Energy Consumption underlies and prioritizes most other costs
  Energy requires less data to understand (3-4 data streams per building)
Desire for quick-wins shifted focus again, to creation of a “demo”

## Slide 11: SBD Business Understanding
23 Feb 2015
5 March 2015
3 April 2015

## Slide 12: SDB Data Understanding - Overview
Acquisition of data took time
Used R, Python, and sometimes Excel (not on Azure)
Delivered 1.5 TB of data in 9 SQL DBs
Approximately 500k (over 5000 per building or 14 per person!) data streams in 92 Puget Sound buildings
But only needed about 10-20 per building for first part of energy analysis phase
Data range was from 1 Jan 2013 to 31 Dec 2014

## Slide 13: SDB - Data Understanding - Data Flow

## Slide 14: SDB Data Understanding – Building Data
Sampled at 1-10 minutes per stream depending on data type
All streams were missing data, up to 3 month gaps existed, most streams have between 20 and 80 percent coverage

## Slide 15: SDB Data Understanding – Weather Data
Weather Data from Weather Underground
10 values – including temperature, dewpoint, windspeed, humidity and some other – available as CSV
Not all stations have all data, or at all times
Took 4 weather stations in the Bellevue/Redmond/Kirkland area with continuous data back to 2009
Weather Data Gaps moved in the 1-2 percent range

## Slide 16: SBD – Data Understanding Challenges
Large amount of data – 9 SQL DB between 320 and 160 GB
Unified over SQL view but was slow (could not build index over data)
Merging to one DB ran afoul of slow SQL Server, decided to switch to Hive
Exported to Hive – SIS output UCS-16
  Noticed too late, made Hive twice as slow
Had to redo as UCS-8: 1.7 TB => 0.88 TB

## Slide 17: SDB - Data Understanding - Reports

## Slide 18: SDB - Data Understanding - Results

## Slide 19: SDB – Data Preparation - Overview
Weather data gathered and consolidated
  Weather data in 3-5 minute intervals
  Averaged and gathered into 15 minute chunks
  Eliminated Nas Gaps covered by
    averaging weather stations
    Interpolating few remaining gaps
Building data gathered and consolidated
  Energy data in variable
  Averaged and gathered into 15 minute chunks
  Created heating degrees and cooling degree variables
Added time data
  Marker for holidays
  Conversion of time into decimal time for easier mathematical manipulation
End result is data for AML

## Slide 20: SDB – Data Preparation – Data flow

## Slide 21: SDB – Data Preparation – Challenges
Data Understanding increased enormously, many surprises
Spline fitting turned out not to work so well, abandoned
Hard to find weather stations with complete coverage
Looking for at least 6 years of coverage, 10 would be better

## Slide 22: SDB – Data Preparation – Reports

## Slide 23: SDB – Data Preparation – Results

## Slide 24: SDB Modeling - Overview
  Considered different architectures
  Went with Standard R and AML in the end
  Many choices available today
    Classic regression and optimization
    Ensemble methods (Boosted Trees, Random Forests, etc.)
    Other ML methods (NN, DNN, SVM, etc.)
    Time Series forecasting (ARIMA)
  Went with Ensemble methods as the are powerful, tolerant to missing data, and new and exciting 

## Slide 25: SDB – Modeling - Architecture

## Slide 26: SDB – Modeling - Challenges
92 buildings made modeling all buildings in AML practically impossible, only modeled about 20
No markup facilities in AML made reporting difficult
Wide variation in results over different buildings
Difficult to encompass results from 92 buildings

## Slide 27: SDB – Modeling - Reports

## Slide 28: SDB – Modeling – Results (City Center)

## Slide 29: SDB – Modeling – Results (City Center)

## Slide 30: SDB – Modeling – Results (Millenium D)

## Slide 31: SDB Evaluation - Overview
Evaluated results by setting up web service, running a simulation, and retrieved values
AML Boosted Tree performed best of methods tried, but this is ongoing

## Slide 32: SDB Evaluation - Architecture

## Slide 33: SDB – Evaluation- Results

## Slide 34: SDB – Modeling – Results – all buildings compared
All 109 buildings, R2<0 eliminated
92 buildings left
Top (blue) is etot.R2
Middle (green) is peak.etot.R2
Bottom (pink) is avg.etot.R2

## Slide 35: SDB – Evaluation- Results

## Slide 36: SDB Deployment - Overview
Weather Forecasts must be integrated
Needs rational reproducible architecture
Pilot needed to show if returns can actually be realized

## Slide 37: SDB Deployment - Architecture

## Slide 38: 88 Acres – Deployment Target Architecture
Azure Machine Learning
Smart Building Platform Services
Weather API’s
Graph-related API’s
Energy API’s
Fault API’s
Location API’s
Power BI
Drop By (Bert’s App)
Weather APP
Cache + Historical & Forecast
Energy APP (ML)
Cache + Historical & Forecast
Fault APP (ML)
Cache + Historical & Forecast
Smart Building Energy Console
ENERGY
Actuals
Forecast
WEATHER
oF
Azure Data Lake
STREAM
STREAM
Enterprise Data Directory
SQL/SQL Azure
R/O
Copy
Buildings
Weather
Energy
Faults
Iconics
Other
Azure IoT/Event Hub/Service Bus
Building
Energy Models
Building
Energy Models
Building
Fault Models
Building
Fault Models

## Slide 39: Current Work
Deploy current AML models into 88 acres production Dashboard
Add control variables to predictive model for peak mitigation
Predictive Maintenance work on Chillers (most expensive and critical piece of an HVAC system)
Create an aggregate clustered building model
Smart Building Energy Console
ENERGY
Actuals
Forecast
WEATHER
oF
Notes: In the future for energy prediction we are looking at a few things, listed above in the order we are attacking.
One is an aggregated cluster model that will allow us to do a few things
1 – Evaluate the relative efficiency of a building in relation to similar buildings
2 – Start out making predictions for a building before we gather data
3 – Make overall energy usage predications for a general group of buildings without actually having data for those buildings.

## Slide 40: Next Steps
Design/ Document/Deploy Pilot
Obtain more data (2015 H1 data)
Add control variables to model and re-train
Investigate automated model creation for AML
Design feasible AML pipeline for 88 Acres Engineers